Annotations-1-43-2010

Prospects of using LNG in gaso-diesel engines on river ships in Siberia/ Epifanov V.S. // River transport (XXI century).2010- № 1(43). – p. 58

Explaines effectiveness of using steam phase after LNG’s vaporizer to supply main tugboats’ gaso-diesel engines (with power 1000 kW and more). Shows time recoupment’s difference between prices for diesel and LNG, which using on river ships on line Yakutsk-Olekminsk-Yakutsk. Writes conditiones to successful using Natural Gas to supply

ships’ power plants in Siberia

Key words: Liquified Natural Gas (LNG), diesel fuel, gasodiesel engine, river ship, ship’s power plant, recoupment.

Contacts: vsepifanov@mail.ru

Stability of right-angled stepped-variable thickness plate / Baryshnikov S.O., Goloskokov D.P. // River transport (XXI century).2010- № 1(43). – p. 62

Researches effectivness of combined work (means stability) of ship’s skin plates and laided on fixed lines. Considers example, when laided on line’s middle point is located above fore-and-aft bulkhead. Shows that this kind of fix doesn’t bring down line’s carrying capacity.

Key words: stability of a plate, strengthening, body repair, wear, critical load.

Contacts: Pantina05@yandex.ru

Modern info-communication technologies in inland water transport of Russia

/ Sykarev A.A., Karetnikov V.V. // River transport (XXI century).2010- № 1(43). – p. 65

Describes features of Karetnov-Sikarev’s approximation model to direct detection of

check-corrective station’s range and to take into account transceiving equipment’s parameters.

Key words: check-corrective station, transceiving equipment, approximation model, range.

Contacts: Pantina05@yandex.ru

About necessity of public relief of energy conservation in transport field/ Mineev V.I. // Речной транспорт // River transport (XXI century).2010- № 1(43). – p. 68.

Considers the questions of energy conservation in water transport field.

Key words: public relief, energy conservation, water transport.

Contacts: nauka@aqua.sci-nnov.ru

The methodology of operational planning of river cargo fleet work on the market.

/ Platov A.Y. // River transport (XXI century).2010- № 1(43). – p. 71.

Describes necessity of revision of methodology of operational planning of river cargo fleet work for the purpose of increasing shipowners’ competition. Shows calculating results which confirm suitability of new methodology introduction. Fixes scales of its profitability.

Key words: methodology, economically suitability, planning, river cargo fleet.

Contacts: platoff@mail.ru

The system of ship’s work factors for efficient decision-making / Платов А.Ю.// Platov A.Y. // River transport (XXI century).2010- № 1(43). – p. 74.

Describes necessity of development of new factor system to estimate ships’ operational work in modern economical conditions. Offers system of three dimentionless factors, researches it

correctness.

Key words: ship’s work factors, modern economical conditions.

Contacts: platoff@mail.ru

Perspective directions in vibroinsulation / Scherbakova O.V., Romanchenko M.K. // River transport (XXI century).2010- № 1(43). – p. 77.

Analysis of modern Russian and foreign vibroinsulators, its main descriptions and ranges of application.

Key words: analysis, vibroinsulator, range of application.

Contacts: rmk2010@mail.ru

Improvement of rate making order in inland water cargo transportation / Belova O.Y. // River transport (XXI century).2010- № 1(43). – p. 81.

# Offers algorithm of rate making in inland water cargo transportation which uses hang-

# the-expense approach and adjusted for transportation market conditions.

Key words: rates, cargo transportation, inland water transport.

Contacts: 211@irsc.omsknet.ru

Influence of frosty swelling on vertical support walls / Samarin V.F., Kozlovskiy O.G. // River transport (XXI century).2010- № 1(43). – p. 84.

Researches influence of frosty swelling on bank consolidation (vertical support walls)

of Moscow Channel. Writes frosty swelling process and methods to avoid its influence while projecting and building.

Key words:  frosty swelling, bank consolidation.

Contacts: oleg-koz@rambler.ru